44/2006-Rev.1

„QUARTER-TURN” ELECTRIC ACTUATOR

Actuators catalogue component list

| No. | Range Gama | Actuator Type red. | Tech. datasheet Nr.fisa the. | Date Data |
| --- | --- | --- | --- | --- |
| 1 | “QUARTER-TURN” actuators for industrial fittings of NOTOR R ST and NOTOR ST type | NR 3ST(N 3ST) | 724a | 01.09.2006 |
| 2 |  | NR 4ST(N 4ST) | 549a | 04.09.2006 |
| 3 |  | NR 5.2ST(N 5.2ST) | 1031a | 04.09.2006 |
| 4 |  | NR 6ST(N 6ST) | 514a | 04.09.2006 |
| 5 |  | NR 7ST(N 7ST) | 728a | 04.09.2006 |
| 6 |  | NR 8ST(N 8ST) | 729a | 05.09.2006 |
| 7 |  | NR 9ST(N 9ST) | 661b | 05.09.2006 |
| 8 |  | NR 10ST(N 10ST) | 1437b | 06.09.2006 |
| 9 |  | NR 11ST(N 11ST) | 1438b | 06.09.2006 |
| 10 |  | NR 12ST(N 12ST) | 99a | 08.09.2006 |

1. Sizes

2. Technical Features

- Output torque…………………………………………………  400 N.m

- Stroke…………………………………………………………. …….90(

- Stroke period……………………………………………………   44 sec

- Motor type………………………………………...       for NR3ST-TAR

…….        for N3ST-ASI

- Motor power………………………………………………….   0,12 kW

- Motor speed…………………………………………….    1500 rev/min

- ISO 5211 type fixing……………………………………..….    F07;F10

- Weight………………………………………………………..    11,8 kg

3. Designation

- SIZES

2. TECHNICAL FEATURES

3. DESIGNATION

1. Sizes

2. Features

- Output torque…………………………………………………         1800 Nm

- Stroke…………………………………………………………………       90(

- Stroke period……………………………………………………….          49 s

- Motor power…………………………………              For N R 5.2ST-0,8Kw

- For  N 5.2 ST-0,75 Kw

- Motor speed……………………………………………...          1500 rev/min

- Motor type: ……………..CM (single phase asynchronous); ASI-for N5.2ST

ASFM(three-phase asynchronous)-(120 drives /hour) for NR5.2ST

- ISO 5211 type fixing…………………………………….          F12; F14;F16

- Weight…………………………………………………………….          65kg

3. Designation

1. SIZES

2. TECHNICAL FEATURES

- Output torque……………………………………………………   2500 N.m

- Stroke…………………………………………………………. ………..  90(

- Stroke period…………………………………………………. .….   37,5 sec

- Motor type……………………………………………        TAR-for NR 6ST

- ASI-for N6ST

- Motor power………………………………………………….. …..    1,1 kW

- Motor speed………………………………………………...     1500 rev/min

- ISO 5211 type fixing………………………………………..    F12;F14;F16

- Weight……………………………………………………………....     70kg

3. DESIGNATION

1. Sizes

2. Technical Features

- Output torque[N.m]…………………………………………….   3200

- Stroke……………………………………………………………...  90(

- Stroke period[sec]………………………………………………...   43

- Motor type………………………………………      TAR-for NR 7ST

- ASI-for N 7ST

- Motor power…………………………………………………   1,1 Kw

- Motor speed[rev/min]………………………………………….    1500

- ISO 5211 type fixing…………………………………..   F12;F14;F16

- Weight…………………………………………………………    83kg

3. Designation

1. Sizes

2. Technical Features

- Output torque[N.m]……………………………………………4300      6000

- Stroke…………………………………………………………… 90(        90(

- Stroke period[sec]……………………………………………… 24           17

- Motor type………………………………………………….   ASI-for N 8ST

- ASFM-for NR 8ST

- Motor power[Kw]………………………………….…..……    3 –for N 8ST

- .                3,2-for NR8ST

- Motor speed[rev/min]………………………………………………..     1500

- ISO 5211 type fixing…………………………………………………      F25

- Weight[kg]…………..……………………………………………….      137

3. Designation

1. Sizes

1. Sizes

1. Sizes

1. Sizes

# Text boxes

MECANISME ELECTRICE PENTRU ACTIONAREA        ROBINETILOR SFERT DE TURA

## ELECTRIC ACTUATORS FOR QUARTER-TURN VALVES

TIP/TYPE

# NOTOR  ST

3

„QUARTER-TURN” ELECTRIC ACTUATOR

###### NR 3 ST

(N3ST)

57-63 Bobalna Street; 2150 Campina; Romania

Tel.40-244-335651; 335652;336571

Fax.40-244-370338;40-244-336641

E-mail:office@ neptun-gears.ro

Website:www.neptun-gears.ro

rev.1

| NO. | 724 a |
| --- | --- |
| Date | 01.09.2006 |

### CARACTERISTICI TEHNICE

Puterea nominala                                             4 KW

Turatia de intrare                                             375 rpm

Raport  nominal                                                 22

Motor electric               ASR200L-16-4KW/375 IMB5

Masa     				                           330Kg

4

| NR3ST(N3ST) – 400 – 28 / 90 – 63 - F12 / 1 / 50 – A – 1E |
| --- |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Equipment var. |
| Type and size |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Output torque [N.m] |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Slat poz. |
| Stroke period [sec] |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Size code |
| Stroke [°] |  |  |  |  |  |  |  |  |  |  |  | Drive form |
| Motor gauge |  |  |  |  |  |  |  | Fixing flange – ISO 5211 |

„QUARTER-TURN” ACTUATOR

###### NR 4ST

###### (N 4 ST)

| NO. | 549a |
| --- | --- |
| Date | 04.09.2006 |

- Output torque…………………………………………………   800 N.m

- Stroke………………………………………………………….           90(

- Stroke period………………………………………………14,6;26,4 sec

- Motor power………………………………………………0,25;0,37 Kw

- Motor type………………………………………….    TAR-for NR 4ST

- ASI- for N 4ST

- Motor speed……………………………………………...  1500 rev/min

- ISO 5211 type fixing…………………………………….   F10;F12;F14

- Weight…………………………………………………………….  25kg

Drawn up by: D.Calugaru

Approved by: C-tin Padure

| NR 4ST(N4ST) – 300 – 13,2 / 90 – 71 - F12 / 1 / 30 – A – 1E |
| --- |
| Type and size |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Equipment var. |
| Output torque [N.m] |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Slat poz. |
| Stroke period [sec] |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Size code |
| Stroke [°] |  |  |  |  |  |  |  |  |  |  |  | Drive form |
| Motor gauge |  |  |  |  |  |  |  | Fixing flange – ISO 5211 |

5

| NO. | 1013a |
| --- | --- |
| Date | 04.09.2006 |

„QUARTER-TURN” ELECTRIC ACTUATOR

### N R 5.2ST

###### (N 5.2ST)

6

| NR 5.2ST( N5.2ST) – 1800 – 49 / 90 – 90 - F14 / 3 / 32 – …. – 3ET |
| --- |
| Type and size |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Equipment var. |
| Output torque [N.m] |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Slat poz. |
| Stroke period [sec] |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Size code |
| Stroke [°] |  |  |  |  |  |  |  |  |  |  |  | Drive form |
| Motor gauge |  |  |  |  |  |  |  | Fixing flange – ISO 5211 |

„QUARTER-TURN” ACTUATOR

###### NR 6ST

###### (N 6 ST)

| NO. | 514a |
| --- | --- |
| Date | 04.09.2006 |

### CARACTERISTICI TEHNICE

Puterea nominala                                             4 KW

Turatia de intrare                                             375 rpm

Raport  nominal                                                 22

Motor electric               ASR200L-16-4KW/375 IMB5

Masa     				                           330Kg

| NR 6ST(N6ST) – 2500 – 37,5 / 90 – 90 - F12 / 1 / 30 – A – 1E |
| --- |
| Type and size |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Equipment var. |
| Output torque [N.m] |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Slat poz. |
| Stroke period [sec] |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Size code |
| Stroke [°] |  |  |  |  |  |  |  |  |  |  |  | Drive form |
| Motor gauge |  |  |  |  |  |  |  | Fixing flange – ISO 5211 |

7

„QUARTER-TURN” ELECTRIC ACTUATOR

###### NR 7ST

###### (N 7 ST)

| NO. | 728a |
| --- | --- |
| Date | 04.09.2006 |

8

| NR 7ST(N7ST) – 3200 – 43 / 90 – 90 - F16 / 1 / 60 – A – 1E |
| --- |
| Type and size |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Equipment var. |
| Output torque [N.m] |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Slat poz. |
| Stroke period [sec] |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Size code |
| Stroke [°] |  |  |  |  |  |  |  |  |  |  |  | Drive form |
| Motor gauge |  |  |  |  |  |  |  | Fixing flange – ISO 5211 |

„QUARTER-TURN” ELECTRIC ACTUATOR

###### NR 8ST

###### (N 8 ST)

| NO. | 729a |
| --- | --- |
| Date | 05.09.2006 |

9

| NR 8ST(N8ST) – 6000 – 17 / 90 – 100 - F25 / 1 / 60M – A – 1E |
| --- |
| Type and size |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Equipment var. |
| Output torque [N.m] |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Slat poz. |
| Stroke period [sec] |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Size code |
| Stroke [°] |  |  |  |  |  |  |  |  |  |  |  | Drive form |
| Motor gauge |  |  |  |  |  |  |  | Fixing flange – ISO 5211 |

„QUARTER-TURN” ELECTRIC ACTUATOR

###### NR 9ST

###### (N 9 ST)

| NO. | 661b |
| --- | --- |
| Date | 05.09.2006 |

2.Technical Features

- Output torque…………………………………………… 8000  |  6000 Nm

- Stroke…………………………………………………………..............  90(

- Stroke period……………………………………………..…...           63 sec

- Motor type……………………………………………   ASFM-for NR 9ST

- ASI-for N 9ST

- Motor power………………………………   For N 9ST….1,5   |    1,1  Kw

- For NR 9ST…...1,6  |    1,25 Kw

- Motor speed……………………………………………….     1500 rev/min

- ISO 5211 output flange……………………………………….……….  F25

- Mass….…………………………………………….…. … 196    |    192 kg

3. Designation :

| NR 9ST(N9ST) | - | 8000 | - | 63 | / | 90 | - | 90 | - | F25 | / | 1 | / | 80 | - | A | - | 3E |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Type and size |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Equipment var. |
| Output torque [N.m] |  |  |  |  |  |  |  |  |  |  |  |  |  | Slat poz. |
| Stroke period [sec] |  |  |  |  |  |  |  |  |  |  |  | Size code |
| Stroke [°] |  |  |  |  |  |  |  | Drive form |
| Motor gauge |  |  |  | Fixing flange – ISO 5211 |

„QUARTER-TURN” ELECTRIC ACTUATOR

###### NR 10ST

###### (N 10ST)

| NO. | 1437b |
| --- | --- |
| Date | 06.09.2006 |

2.Technical Features

- Output torque………………………………………….  10000 Nm

- Stroke…………………………………………………………...90(

- Stroke period……………………………………………… 114 sec

- Motor type…………………………………    ASFM-for NR 10ST

- ASI-for N 10ST

- Motor power……………………………      For N 10ST….1,5 Kw

- For NR 10ST…...1,6 Kw

- Motor speed………………………………………… 1500 rev/min

- ISO 5211 output flange……………………………………..….F25

- Mass….…………………………………………….……… 250 kg

3. Designation :

| NR 10ST(N10ST) | - | 10000 | - | 114 | / | 90 | - | 90 | - | F25 | / | 1 | / | 80 | - | A | - | 3E |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Type and size |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Equipment var. |
| Output torque [N.m] |  |  |  |  |  |  |  |  |  |  |  |  |  | Slat poz. |
| Stroke period [sec] |  |  |  |  |  |  |  |  |  |  |  | Size code |
| Stroke [°] |  |  |  |  |  |  |  | Drive form |
| Motor gauge |  |  |  | Fixing flange – ISO 5211 |

„QUARTER-TURN” ELECTRIC ACTUATOR

###### NR 11ST

###### (N 11ST)

| NO. | 1438 b |
| --- | --- |
| Date | 06.09.2006 |

2.Technical Features

- Output torque…………………………………………..  16000 Nm

- Stroke…………………………………………………………... 90(

- Stroke period………………………………………………  152 sec

- Motor type…………………………………     ASFM-for NR 11ST

- ASI-for N 11ST

- Motor power……………………………       For N 11ST….1,5 Kw

- For NR 11ST…...1,6 Kw

- Motor speed…………………………………………  1500 rev/min

- ISO 5211 output flange……………………………………..…. F25

- Mass….…………………………………………….………  374 kg

12

3. Designation :

| NR 11ST(N11ST) | - | 16000 | - | 152 | / | 90 | - | 90 | - | F25 | / | 1 | / | 80 | - | A | - | 3E |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Type and size |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Equipment var. |
| Output torque [N.m] |  |  |  |  |  |  |  |  |  |  |  |  |  | Slat poz. |
| Stroke period [sec] |  |  |  |  |  |  |  |  |  |  |  | Size code |
| Stroke [°] |  |  |  |  |  |  |  | Drive form |
| Motor gauge |  |  |  | Fixing flange – ISO 5211 |

„QUARTER-TURN” ELECTRIC ACTUATOR

###### NR 12ST

###### (N 12ST)

| NO. | 99a |
| --- | --- |
| Date | 08.09.2006 |

2.Technical Features

- Output torque…………………………………………..  22300 Nm

- Stroke…………………………………………………………... 90(

- Stroke period………………………………………………  348 sec

- Motor type…………………………………     ASFM-for NR 12ST

- ASI-for N 12ST

- Motor power…………………………………………………. 4 Kw

- Motor speed…………………………………………  1500 rev/min

- ISO 5211 output flange……………………………………..…. F25

- Mass….…………………………………………….………  435 kg

13

3. Designation :

| NR 12ST(N12ST) | - | 22300 | - | 348 | / | 90 | - | 112 | - | F30 | / | 1 | / | 80 | - | A | - | 3E |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Type and size |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Equipment var. |
| Output torque [N.m] |  |  |  |  |  |  |  |  |  |  |  |  |  | Slat poz. |
| Stroke period [sec] |  |  |  |  |  |  |  |  |  |  |  | Size code |
| Stroke [°] |  |  |  |  |  |  |  | Drive form |
| Motor gauge |  |  |  | Fixing flange – ISO 5211 |

Mecanismele tip NOTOR ST si NOTOR R ST

se folosesc pentru actionarea electrica a robinetelor industriale sfert de tura, precum si pentru alte aplicatii .

1. Conditii de utilizare a mecanismelor

-tensiuni de alimentare:

-standard: 380 V.

-la cerere: 220 V; 400 V; 500 V.

-frecventa retelei:

-standard: 50 Hz.

-la cerere: 60 Hz.

-numar maxim de porniri pe ora: 6 pentru NOTOR ST

:120…1200 pentru NOTOR R ST

-temperatura mediului ambiant:

-pentru mecanism:

-standard: -20°C……+45°C.

-la cerere: -40°C……+40°C.

-pentru cofretul electric:

-standard:   -5°C..…..+40°C.

-la cerere: -29°C……+40°C.

-executie speciala pentru climat tropical umed TH, conform STAS 6692-83.

-puterea maxima a motorului electric: 4kW.

-turatia motorului electric: 1500 rot/min.

-gradul de protectie mecanica: IP 54.

-variante de executie:

-normala: N

2. Caracteristici constructive

Mecanismele tip NOTOR ST si NOTOR R ST includ urmatoarele subansamble de baza:

-mecanism  multitura NOTOR A/C

-reductor melcat sfert de tura tip AMS

3.Caracteristici tehnice si dimensiuni conform fise  anexate

NOTOR ST and NOTOR R ST electric actuators are designed to drive “quarter-turn” industrial valves or any other applications.

1. Actuators operating conditions

- supply voltages:

- standard: 380 V.

- on request: 220 V; 400 V; 500 V.

- frequency:

- standard: 50 Hz.

- on request: 60 Hz.

- maximum number of starts per hour: 6 for NOTOR ST

:120….1200 for NOTOR R ST

- ambient temperature:

- for the actuator:

- standard: -20°C……+45°C.

- on request: -40°C……+40°C.

- for the electric switch box:

- standard:   -5°C..…..+40°C.

- on request: -29°C……+40°C.

-specialTH manufacturing available for the tropical rainy climate according to STAS 6692-83.

- maximum power of the electric motor: 4kW.

- electric motor speed: 1500 rot/min.

- mechanical protection level: IP 54.

- manufacturing variants available:

- normal: N

2. Constructive features

NOTOR ST and NOTOR R ST actuators include the following basic subsets:

- NOTOR A/C multi-turn actuator

- AMS type quarter turn worm gearbox

3.Technical features and sizes according to the datasheets attached